## Slide 1
BY : Yasmeen Yasser Mohamed
Supervised by : Eng. Mahmoud Samir
Eng. Shehab Ahmed
SMART HOME SYSTEM

## Slide 2: FRONT: 1-home door. 2-garage door. 3-LDR to detect the time (morning, evening, in between). 4-bell. 5-3 ststes leds .
Air conditioner:
We represent it as motor
It has two modes:
1-the system control it by comparing the temperature with the temperature read by the temperature sensor
2-the user could control it by switch
TV:
We represent it as led
HOME CONTINTES
4 Rooms:
We represent it as Leds

## Slide 3: OUR HOME IN PROTEUS
1st FLOOR:
Panoramic window allows natural light to flow into the house
2nd FLOOR:
Stone tiling is delightfully accompanied by soft grey tones
3rd FLOOR:
Large terrace finished in cool grey for the perfect neutral effect
ROOF:
Stepped rear design offers attractive viewing profile

## Slide 4: Drivers Used:
Door MCU:
-BIT_MATH LIB
-STD_TYPES_LIB
-Smart Home-CONFIG LIB -DIO DRIVER
-ADC DRIVER
-LCD DRIVER
-KPD DRIVER
-TIMER1 DRIVER
-UART DRIVER
MASTER MCU:
-BIT_MATH LIB
-STD_TYPES_LIB -DIO DRIVER
-LCD DRIVER
-KPD DRIVER
-SPI DRIVER
-UART DRIVER
SLAVE MCU:
-BIT_MATH LIB
-STD_TYPES_LIB
-Smart Home-CONFIG LIB -DIO DRIVER
-ADC DRIVER
-EXT_INT0 DRIVER
-LCD DRIVER
-SPI DRIVER

## Slide 5: FIREST MICROCONTROLLER FUNCTIONS: (Door MCU)
1-SELECT MODE
2-GUEST MODE
3-ADMIN MODE
3-LDR
Evening(it is dark)
In between (there is little light)
Morning(it is light)

## Slide 6: Door Functions
If he log in correctly as Guest:
1-guest led will turn on
2-the bell will ring for 1 minute.
3- the master microcontroller will say that there is a gust here.
4-bell and guest led will turn off .
3rd Floor
1-Log in system:
-after choosing admin mode or guest mode the user must enter correct password , the system will give the user number of tries it is configurable could change very easy .
-if user take all of his
tries he will enter the block mode (for 2 minutes), then he will try again.
Ex: if he have 3 tries:
If he log in correctly as admin:
1- admin led will turn on.
2-he will choose if he want to enter the home or rhe garage.

## Slide 7: Admin mode cont.
If he choose Garag:
The garage door will open for 1 minute
Then close again and admin led will turn off.
If he choose home:
The home door will open for 1 minute to let him get in .
after the door close
the door
Microcontroller till
the master that
there is admin get
in to make him start it ‘s functions.

## Slide 8
If the user enter any wrong choice the system will detect that and make him choose again.
NOTE THAT:
This happen every ware throw the system.

## Slide 9: AFTER the admin enter the home the Master microcontroller will start working:
If the user press enter’=‘ the system will change the welcome page and move to the options

## Slide 10
The admin could control that:
-Room1
-Room2
-Room3
-Room4
-TV
-AIR condationer
Admin mode:

## Slide 11: Admin mode:
Room1
Room2
Room4
Room3

## Slide 12: Admin mode:
TV
Air Conditioner

## Slide 13
The guest could control that:
-Room1
-Room2
-Room3
-Room4
Guest mode:

## Slide 14: Guest mode:
Room1
Room2
Room4
Room3

## Slide 15: Anytime if the user feel that he didn’t need to use the system anymore he could return to moodes page and press enter ’=‘ so in this time the system will stop taking orders and waiting for new action come to him from the door MCU

## Slide 16: Now the Slave MCU WILL START FUNCTION
When the Master MCU Take the order he will send it to the slave MCU TO Execute him:
1-it will light the Rooms on and off.
2-it will turn tv on or off.
3-it will read the temperature sensor and decide if it will turn the air conditioner on or not .
4- any time the switch pressed it will turn air conditioner on no matter the room temperature.
5-it will display any action on the screen.

## Slide 17: THANK YOU.